# Device Summary

The following table summarizes the types of backflow prevention devices discussed in the lesson.

| Device | Type | Features | Limitations | Applications |
| --- | --- | --- | --- | --- |
| Air Gap | Physical | Unobstructed, vertical air space separates a potable system from a non-potable system. | Interruption in piping creates a subsequent pressure drop on the "downstream" portion. | At the end of the supply line or faucet such as at a sink, vat, or storage tank |
| Barometric Loop | Physical | Extension of the supply line shaped like a giant upside-down "U”. | Must be at least 35 feet tall, and the base must be at a higher elevation than any of the inlets or fixtures on the downstream side of the loop. Protects against back-siphonage only. | Industrial plant hose system |
| Hose Bibb Vacuum Breaker (HBVB) | Mechanical | A spring-loaded valve and an atmospheric vent that is controlled by a diaphragm seal. | Cannot be used under continuous pressure because the spring-loaded valve may stick in the open position. | Hose bibbs, service sinks, hydrants |
| Atmospheric Vacuum Breaker (AVB) | Mechanical | Float valve that moves up and down on a shaft (not spring loaded). Water moving in the normal direction of flow lifts the float and causes the atmospheric vent to close. | Protects against back-siphonage only. | Faucets |
| Pressure Vacuum Breaker (PVB) | Mechanical | Similar to the AVB but instead has two test cocks, two gate or ball valves for testing the unit, and two spring-loaded valves. | Protects against back-siphonage only. | Lawn sprinklers, livestock water systems, pesticide spray tanks & filling systems, swimming pools, laboratory equipment |
| Backflow Preventer With Intermediate Atmospheric Vent | Mechanical | Atmospheric vent between two check valves that are spring loaded for automatic closure under static conditions. | Cannot be tested. Not all types are approved for continuous pressure. | Supply lines for laboratory equipment, food processing tanks, sterilizers, dairy equipment, livestock drinking fountains, residential boilers |
| Reduced Pressure Zone Backflow Prevention Assembly (RPZ) | Mechanical | Two independent, spring-loaded check valves with a reduced pressure zone between them. | Must be mounted in a location where the relief valve drain will not become flooded. | Main supply lines, food cookers, lawn sprinklers, and fire sprinklers |
| Double Check Valves | Mechanical | Two check valves that are spring loaded in the closed position. | Approved for limited use with low-hazard, continuous pressure conditions. | Supply lines, fire protection sprinklers, tanks and vats, food cookers |

## Examples of Cross-Connections and Appropriate Protections

The following table provides examples of some of the types of equipment with potentially submerged inlets and possible backflow/back-siphonage protection.

| Equipment | Backflow/Back-Siphonage Preventer |
| --- | --- |
| Boiler with chemicals added | Reduced pressure device |
| Boiler with no chemicals added | Backflow preventer with intermediate atmospheric vent |
| Carbonator for beverage dispenser | Backflow preventer with intermediate atmospheric vent |
| Flush valve toilet | Air gap, atmospheric or pressure vacuum breaker |
| All hose bibbs inside and outside of establishment | Hose bibb vacuum breaker |
| Preflush hose with a nozzle head that may be submerged | Pressure vacuum breaker. (If the preflush hose is spring loaded to automatically create an air gap when released, no backflow device is required.) |
| Perforated pipe to wok cooker | Atmospheric vacuum breaker |
| Supply inlet to garbage grinder installed after the last shut off valve | Atmospheric vacuum breaker |
| Supply inlet to dish table trough installed after the last shut off valve | Atmospheric vacuum breaker |
| Fill line for steam kettle installed after the last shut off valve | Atmospheric vacuum breaker |
| Supply line for mechanical warewashing machine installed after the last shut off valve | Atmospheric vacuum breaker |
| Supply line to all soap and chemical dispensing units on mechanical warewashing machine installed after the last shut off valve | Atmospheric vacuum breaker |
| Garbage can washer installed after the last shut off valve | Atmospheric vacuum breaker |
| Soap portioner on faucet | Air gap |
| Water wash system for exhaust hood | Backflow preventer with intermediate atmospheric vent or reduced pressure zone backflow prevention assembly |

## Food Industry Applications

Table lists appropriate cross-connections for drains or waste lines for food service equipment.

| Food Service Equipment | Cross-Connection for Drains or Waste Lines |
| --- | --- |
| Booster heater for warewashing machine | Air gap between the relief valve vent pipe and the floor drain or floor sink |
| Water-cooled compressor for an ice machine or other refrigeration system | Air gap between the end of the supply line and the floor drain or floor sink |
| Drain lines for: Salad cooler table or salad bar Soda fountain/dispenser ice bin Steam kettle or steam table | Air break |
| Condensate drain lines for refrigeration equipment | Air break |
| Water softener with a brine tank that drains through a hose bibb | Hose bibb vacuum breaker |
| Water softener with a brine tank with a gate or ball valve | Air gap |

# Plumbing Controls for Commercial Food Establishments

# Lesson: Protection for Drains, Wells, and Septic Systems

## Lesson Overview

This lesson describes the importance of and protection measures for drains, wells, and septic systems.

After completing this lesson, you should be able to:

- Identify cross-connection control methods for drains.

- Describe the purpose and operating principles of grease traps and interceptors.

- Describe different types of well construction and how they operate.

- Indicate methods for protecting wells from contamination.

- Identify risks related to septic systems and ways to minimize those risks.

- Identify indicators of septic system problems.

## Introduction

This lesson will present information on preventing water supply contamination from:

- Drains.

- Grease interceptors and traps.

- Wells.

- Septic systems.

## Drains: Indirect Connections

There are two types of cross-connections for drains: indirect and direct.

An indirect connection between the water supply or food service equipment and the facility’s drainage or wastewater disposal system is necessary in most cases to prevent wastewater from backflowing into the supply or into equipment where food, kitchenware, or utensils are retained.

An indirect connection is a waste line or pipe from a fixture, receptacle, or device that discharges used water, waste materials, or sewage into the facility’s drainage system through an air gap (discussed in the previous lesson) or an air break.

An air break is a waste line or pipe from a fixture that discharges used water or liquid waste into another fixture or receptacle at a point below the flood level rim, such as the waste line from a vegetable preparation sink that drains into a floor drain.

## Drains: Direct Connections

A direct connection is a waste line or pipe from a fixture, receptacle, or device that discharges used water, waste materials, or sewage directly into the facility’s drainage system.

A direct connection is permitted in a few limited instances:

- Warewashing machines located within 5 feet of a trapped floor drain may have a direct waste connection to the inlet side of a properly vented floor drain trap.

- Garbage disposals require a direct connection to prevent the solids from separating out from the waste slurry.

- Other exceptions as provided by law or regulation.

## Food Industry Applications

The table below lists appropriate cross-connections for drains or waste lines for various food service equipment.

| Food Service Equipment | Cross-Connection for Drains or Waste Lines |
| --- | --- |
| Booster heater for warewashing machine | Air gap between the relief valve vent pipe and the floor drain or floor sink |
| Water-cooled compressor for an ice machine or other refrigeration system | Air gap between the end of the supply line and the floor drain or floor sink |
| Drain lines for: Salad cooler table or salad bar Soda fountain/dispenser ice bin Steam kettle or steam table | Air break |
| Condensate drain lines for refrigeration equipment | Air break |
| Water softener with a brine tank that drains through a hose bibb | Hose bibb vacuum breaker |
| Water softener with a brine tank with a gate or ball valve | Air gap |

## Grease Interceptors and Traps

Oil and grease from foods and cooking processes entering a facility’s drainage waste system will eventually solidify somewhere downstream and clog the sewer line and/or cause potential problems onsite or in the public sewage system.

To prevent this, oil and grease in wastewater is collected in grease interceptors or grease traps. Grease interceptors are usually installed inside the establishment and may be any size. Grease traps are outside the establishment and must be a minimum of 1,000 gallon capacity.

Types of Oil and Grease

- Dissolved Oil: Oil that has been dissolved in water via a degreasing compound and will not separate from the water.

- Chemically Emulsified Oil: Oil that has been broken down into very small particles via a detergent and will not float to the surface.

- Free Oil: Oil in a liquid form that will consolidate or congeal on the water surface. The majority of the oil produced in a food service facility is free oil.

- Mechanically Emulsified Oil: Free oil that has been agitated in water to form small droplets. These droplets will congeal given sufficient time.

## Grease Trap Size and Location

Grease trap installations are designed and sized based on anticipated flow rates and organic load for maximum efficiency. The size needed depends on:

- Flow rate.

- Ratio of grease to water.

- Suspended solids.

- Frequency of cleaning/emptying.

Regardless of size, the trap should be:

- Properly vented.

- Located as close to the source as possible for ease of cleaning and service without creating a nuisance.

## Wells

The main types of wells are:

- Dug wells, which may be excavated by hand or by machinery. Dug wells may be lined with stone, brick, reinforced concrete, or precast ring wells.

- Driven wells, which are created by hammering a point into the ground, with pipe sections added as needed until groundwater is reached.

- Drilled wells, which are typically created using machinery with drilling stems that are turned to create a cutting action in the ground.

## Reducing Contamination in Wells

Regardless of the type of well used as a water source, the following steps can help reduce the risk of contamination:

- Locate wells a safe distance from sources of contamination.

- Properly cover wells.

- Ensure that well pipes have watertight casings or linings to prevent contamination.

- Conduct sanitary surveys to monitor well safety.

- Provide sanitary protection for springs and disinfection of other water sources.

- Ensure that wells are readily accessible at the top for inspection, servicing, and testing.

Contamination Threats to Wells

Shallow wells, such as dug and driven wells, are relatively easy to contaminate. Possible contaminants include:

- Microorganisms, typically from animal fecal matter. Common microorganism contaminants include E. coli, Salmonella, norovirus, and Giardia.

- Chemicals, including nitrates from fertilizers, pesticides, and organic compounds from gasoline.

- Minerals, including lead leached from old pipes, and naturally occurring arsenic, radon, and uranium.

## Septic Systems

The main components of a septic system are:

- A tank, which is a large concrete box with internal baffles. Inside the tank, oil and grease float to the top, solids sink to the bottom, and the liquid effluent flows out.

- A drainfield line, a system of buried pipes that carry water from the tank to the drainfield, an open area where the soil absorbs the water.

As septic tank effluent percolates through the drainfield, soil microorganisms treat wastewater physically, chemically, and biologically before it reaches the groundwater, preventing pollution and public health hazards. In most cases, the wastewater requires no further treatment before reaching the underlying groundwater level.

## Risks Related to Septic Systems

If the drainfield soil is overloaded with water, or when a specific contaminant cannot be treated by soil microorganisms, the quality of the underlying groundwater may be affected.

When septic systems do not function properly, the risks include:

- Contamination of groundwater by pathogens or toxic chemicals.

- Surfacing of untreated sewage.

- Undesirable algae and plant growth in lakes or streams.

- Insects breeding in wet areas where sewage reaches.

- Degraded air quality.

Indicators of septic system problems include:

- Slow drains.

- Odors.

- Standing water.

- Gurgling sounds.

- Nearby wells testing positive for bacteria.

## Managing Septic System Risks

To minimize risks associated with septic systems, ensure that:

- The septic system is located a safe distance from water sources.

- The septic tank is:

  - Properly sized for average daily flow of sewage, a retention period of approximately 24 hours, and adequate sludge storage (at least 750 gallons).

  - Constructed of durable materials, with a watertight cover that is insect- and rodent-proof and will withstand any load likely to be placed upon it.

- The system incorporates a distribution box and properly constructed disposal field that uses the largest area available.

- The tank permits easy access for inspection and cleaning.

- The septic system is kept free of grease and oil.

- The system is monitored and maintained on a regular basis.

## Resources

Select the following links for more information on plumbing controls for commercial establishments:

- FDA – Food Establishment Plan Review Guide, Plumbing and Cross-Connection Control

- FDA – Pasteurized Milk Ordinance 2007: Appendix D – Standards for Water Sources

- EPA – Cross-Connection Control Manual

## Lesson Summary

This lesson described the importance of and protection measures for drains, wells, and septic systems.

You should now be able to:

- Identify cross-connection control methods for drains.

- Describe the purpose and operating principles of grease traps and interceptors.

- Describe different types of well construction and how they operate.

- Indicate methods for protecting wells from contamination.

- Identify risks related to septic systems and ways to minimize those risks.

- Identify indicators of septic system problems.